## Slide 1: Chapter 2: Boolean Algebra and Logic Gates

## Slide 3: F1= XY’ + X’Z
X | Y | Z | X’ | Y’ | XY’ | X’Z | F1
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
F1

## Slide 4: F2= X’Y’Z + X’YZ + XY’
X | Y | Z | X’ | Y’ | X’Y’Z | X’YZ | XY’ | F2
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 5
X | Y | Z | F1 | F2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
F1
F2= X’Y’Z + X’YZ + XY’
F1= XY’ + X’Z

## Slide 6
F(x, y, z) = xy + x’z + yz
= xy + x’z + yz.1
By Postulate 5(a)
By Postulate 4(a)
By Theorem 2

## Slide 7: CANONICAL FORMS
How to express a boolean function algebraically from a given truth table?
X | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
F(x,y,z)=?

## Slide 8: Summation of Minterms
F(x,y,z)=?
X | Y | Z | Term | Designation | F
0 | 0 | 0 | X’Y’Z’ | m0 | 0
0 | 0 | 1 | X’Y’Z | m1 | 1
0 | 1 | 0 | X’YZ’ | m2 | 0
0 | 1 | 1 | X’YZ | m3 | 1
1 | 0 | 0 | XY’Z’ | m4 | 1
1 | 0 | 1 | XY’Z | m5 | 1
1 | 1 | 0 | XYZ’ | m6 | 0
1 | 1 | 1 | XYZ | m7 | 0

## Slide 9: Summation of Minterms
F(x,y,z)= m1+ m3 + m4 + m5 = X’Y’Z+X’YZ+XY’Z’+XY’Z =∑(1, 3, 4, 5)
X | Y | Z | Term | Designation | F
0 | 0 | 0 | X’Y’Z’ | m0 | 0
0 | 0 | 1 | X’Y’Z | m1 | 1
0 | 1 | 0 | X’YZ’ | m2 | 0
0 | 1 | 1 | X’YZ | m3 | 1
1 | 0 | 0 | XY’Z’ | m4 | 1
1 | 0 | 1 | XY’Z | m5 | 1
1 | 1 | 0 | XYZ’ | m6 | 0
1 | 1 | 1 | XYZ | m7 | 0

## Slide 10: Summation of Minterms
F(x,y,z)= m1+ m3 + m4 + m5 = X’Y’Z+X’YZ+XY’Z’+XY’Z =∑(1, 3, 4, 5)
F’ = m0 + m2 + m6 + m7 = X’Y’Z’+X’YZ’+XYZ’+XYZ
X | Y | Z | Term | Designation | F
0 | 0 | 0 | X’Y’Z’ | m0 | 0
0 | 0 | 1 | X’Y’Z | m1 | 1
0 | 1 | 0 | X’YZ’ | m2 | 0
0 | 1 | 1 | X’YZ | m3 | 1
1 | 0 | 0 | XY’Z’ | m4 | 1
1 | 0 | 1 | XY’Z | m5 | 1
1 | 1 | 0 | XYZ’ | m6 | 0
1 | 1 | 1 | XYZ | m7 | 0

## Slide 11: Multiplication of Maxterms
F(x,y,z)=?
X | Y | Z | Term | Designation | F
0 | 0 | 0 | X + Y + Z | M0 | 0
0 | 0 | 1 | X + Y + Z’ | M1 | 1
0 | 1 | 0 | X + Y’ + Z | M2 | 0
0 | 1 | 1 | X + Y’ + Z’ | M3 | 1
1 | 0 | 0 | X’ + Y + Z | M4 | 1
1 | 0 | 1 | X’ + Y + Z’ | M5 | 1
1 | 1 | 0 | X’ + Y’ + Z | M6 | 0
1 | 1 | 1 | X’ + Y’ + Z’ | M7 | 0

## Slide 12: Multiplication of Maxterms
By MinTerms, F = m1+ m3 + m4 + m5 = X’Y’Z+X’YZ+XY’Z’+XY’Z
F’ = m0 + m2 + m6 + m7 = X’Y’Z’+X’YZ’+XYZ’+XYZ
.
=> F = (X’Y’Z’+X’YZ’+XYZ’+XYZ)’ =(X+Y+Z) (X+Y’+Z) (X’+Y’+Z) (X’+Y’+Z’)
X | Y | Z | Term | Designation | F
0 | 0 | 0 | X + Y + Z | M0 | 0
0 | 0 | 1 | X + Y + Z’ | M1 | 1
0 | 1 | 0 | X + Y’ + Z | M2 | 0
0 | 1 | 1 | X + Y’ + Z’ | M3 | 1
1 | 0 | 0 | X’ + Y + Z | M4 | 1
1 | 0 | 1 | X’ + Y + Z’ | M5 | 1
1 | 1 | 0 | X’ + Y’ + Z | M6 | 0
1 | 1 | 1 | X’ + Y’ + Z’ | M7 | 0

## Slide 13: Multiplication of Max terms
By MinTerms, F = m1+ m3 + m4 + m5 = X’Y’Z+X’YZ+XY’Z’+XY’Z
F’ = m0 + m2 + m6 + m7 = X’Y’Z’+X’YZ’+XYZ’+XYZ
.
=> F = (X’Y’Z’+X’YZ’+XYZ’+XYZ)’ = (X+Y+Z) (X+Y’+Z) (X’+Y’+Z) (X’+Y’+Z’) = M0 + M2 + M6 + M7 = ∏ ( 0, 2, 6, 7)
X | Y | Z | Term | Designation | F
0 | 0 | 0 | X + Y + Z | M0 | 0
0 | 0 | 1 | X + Y + Z’ | M1 | 1
0 | 1 | 0 | X + Y’ + Z | M2 | 0
0 | 1 | 1 | X + Y’ + Z’ | M3 | 1
1 | 0 | 0 | X’ + Y + Z | M4 | 1
1 | 0 | 1 | X’ + Y + Z’ | M5 | 1
1 | 1 | 0 | X’ + Y’ + Z | M6 | 0
1 | 1 | 1 | X’ + Y’ + Z’ | M7 | 0

## Slide 14: Conversion Between Canonical Forms
Boolean functions expressed as a sum of minterms or product of
maxterms are called canonical form
By MinTerms, F = m1+ m3 + m4 + m5 = ∑(1, 3, 4, 5) (function gives 1)
By MaxTerms, F = M0 M2 M6 M7 = ∏ ( 0, 2, 6, 7) (function gives 0)
X | Y | Z | MinTerms | Designation | MaxTerms | Designation | F
0 | 0 | 0 | X’Y’Z’ | m0 | X + Y + Z | M0 | 0
0 | 0 | 1 | X’Y’Z | m1 | X + Y + Z’ | M1 | 1
0 | 1 | 0 | X’YZ’ | m2 | X + Y’ + Z | M2 | 0
0 | 1 | 1 | X’YZ | m3 | X + Y’ + Z’ | M3 | 1
1 | 0 | 0 | XY’Z’ | m4 | X’ + Y + Z | M4 | 1
1 | 0 | 1 | XY’Z | m5 | X’ + Y + Z’ | M5 | 1
1 | 1 | 0 | XYZ’ | m6 | X’ + Y’ + Z | M6 | 0
1 | 1 | 1 | XYZ | m7 | X’ + Y’ + Z’ | M7 | 0

## Slide 15: Function Expression in Canonical Form
Express the Boolean function F = A + B’C as a sum of minterms
(All variables must be present in each term)
Process: 1
In each term, for each missing variable P, multiply (P+P’), until all the variables appear in each term
Finally, if same term appears multiple times, discard multiple copies
F = A + B’C = A(B+B’) + B’C(A+A’)
= AB + AB’ + B’CA + B’CA’
= AB(C+C’) + AB’(C+C’) + B’CA + B’CA’
= ABC + ABC’ + AB’C + AB’C’ + AB’C + A’B’C
= ABC + ABC’ + AB’C + AB’C’ + A’B’C = m7 + m6 + m5 + m4 + m1

## Slide 16: Conversion to Canonical Form
Express the Boolean function F = A + B’C as a sum of minterms.
Process: 2
Draw the Truth Table
Read the minterms from the truth table
F = m1 + m4 + m5 + m6 + m7

## Slide 17: Conversion to Canonical Form
Express the Boolean function F = xy + x’z as a product of maxterms
Process: 1
Convert the function into OR terms using the distributive law
F = xy + x’z
= (xy + x’) (xy + z)
= (x + x’)(y + x’) (x + z)(y + z)
= (x’ + y)(x + z)(y + z)
For each missing variable P, add the PP’ with each term, until all the variables appear in each term.
F = (x’ + y)(x + z)(y + z) = (x’ + y + zz’) (x + z + yy’) (y + z + xx’)
= (x’ + y + z)(x’ + y + z’) (x + y + z)(x + y’ + z) (x + y + z)(x’ + y + z)
= (x’ + y + z)(x’ + y + z’) (x + y + z)(x + y’ + z)
Distributive Law:
X(Y+Z) = XY + XZ
X+(YZ) = (X+Y) (X+Z)

## Slide 18: Conversion to Canonical Form
Express the Boolean function F = xy + x’z as a product of maxterms
Process: 2
Draw the Truth Table
Read the maxterms from the truth table
F = M0M2M4M5
X | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 19: Standard Form
Each term in the function may contain one, two, or any number of literals F = y + xy + xyz
Either the sum of products or the products of sums, not both!
F = AB + C(D + E)  Non Standard Form
= AB + CD + CE  Standard Form
Some Standard Functions:
F1 = y’ + xy + x’yz’ (sum of products)
F2 = x(y’ + z)(x’ + y + z’) (product of sums)

## Slide 20: Common Logical operations

## Slide 21: Common Logical operations